## Slide 1
Working volume | 1500 mL
Temperature | 30 ℃
pH | 7.0
Air flow rate | 0.2～0.6 vvm
酵母の共培養によるバイオマスからのエタノールとキシリトールの同時生産
Production of ethanol and xylitol by co-cultivation of yeasts from lignocellulosic biomass
(Kyoto Inst. Tech.) ○Taiki YAMAWAKI・Yoichi KUMADA・Jun-ichi HORIUCHI*
Introduction
Materials and Methods
Candida magnoliae (FERM P-16522)
xylose
xylose
xylitol
xylitol
Energy metabolism
ATP synthesis
Saccharomyces cerevisiae (NBRC1953)
Mannose
Glucose or Maltose
Lectin-like protein
Glucose or Maltose consumption
Xylitol production medium |  | YMP medium | 
Xylose | 30 g/L | Glucose | 30 g/L
YNB | 1.7 g/L | Yeast Extract | 3.0 g/L
Urea | 2.27 g/L | Malt Extract | 3.0 g/L
Casamino Acids | 1.0 g/L | Peptone | 5.0 g/L
pH sensor
pH
controller
NaOH
Air
Peristaltic pump
Working volume: 1500 mL
Co-cultivation
Flocculation
Settlement
Medium replacement
Flocculent yeast
Xylitol-producing yeast
Repeat batch culture with immobilized bacteria
Chart: Time (h)
| 0 | 3 | 18 | 21 | 24 | 27 | 30 | 33 | 45 | 48 | 72 | 96 | 100
キシロース濃度 | 27.3251 | 27.6992 | 21.6264 | 19.5166 | 18.4118 | 19.8594 | 16.8856 | 15.2412 | 10.8412 | 11.2031 | 3.0556 | 0 | 0
キシリトール濃度 | 0 | 0 | 4.124 | 4.88 | 5.808 | 7.7949 | 7.934 | 8.5567 | 11.7239 | 12.9273 | 15.9744 | 16.0598 | 16.6403
OD660 | 0.344 | 0.58 | 3.28 | 2.86 | 3.19 | 3.51 | 3.58 | 3.89 | 4 | 4.93 | 6.13 | 6.92 | 6.72
Time courses of batch fermentation for xylitol production
Results and Discussion
Time courses of repeated batch fermentation for xylitol production by air-lift bioreactor using co-culture of S. cerevisiae and C. magnoliae
Immobilized C. magnoliae
Xylitol concentration, yield, productivity and ethanol productivity of batch fermentation for xylitol production by air-lift bioreactor using co-culture of S. cerevisiae and C. magnoliae
Xylitol productivity : 0.32 g/L/h → 1.20 g/L/h
Metabolic pathway of C. magnoliae
Mechanism of aggregation
Effective biological utilization of biomass
Hemicellulose
Corn cobs
Cellulose
Corn cobs
residue
Acid hydrolysis
Saccharification
Xylose
Glucose
It is important to use both xylose and glucose
・Five-carbon sugar alcohol
・Natural sweetener for
food and medical usage
Forest resources
Xylitol
Chemical
hydrogenation
Industrial xylitol production
・Volatile colorless liquid
・Various uses such as disinfectants
and sterilizers, food additives, fuel, etc.
Industrial ethanol production
Petroleum→Naphtha
Ethylene
Ethanol
Xylitol
Ethanol
Cell immobilization
Enhanced xylitol and ethanol production based on
co-cultivation of xylitol-producing yeast and flocculent yeast
Air-lift bioreactor
Fermentation conditions
Procedure for repeated batch culture based on co-cultivation
Strains
Medium
Sodium alginate | 10 g/L
CaCl2 | 0.1 M
Penicillin G potassium | 5000 Unit/L
Broth
withdrawal
Medium
replacement
Cultivation
Settlement
Procedure for repeated batch culture based on co-cultivation
Batch culture for xylitol production by air-lift
Co-cultivation using C. magnoliae and flocculent yeast
Flocculent yeast
Co-cultivation
Settlement
Withdrawal of culture broth
Medium replacement
C. magnoliae
S. cerevisiae
Chart: Time (h)
| 0 | 20 | 45 | 67.5
Xylose | 26.8 | 17.3 | 8.21 | 1.92
Xylitol | 0 | 4.6 | 12.7 | 16.8
Glucose | 0 | 0 | 0 | 0
Ethanol | 9.91 | 7.68 | 5.89 | 4.57
xylose2 | 27.9 | 24.4 | 16.7 | 3.13 | 0.14
xylose3 | 25.6 | 24.1 | 14 | 2.87 | 0.04
xylose4 | 26.7 | 25.2 | 16.2 | 4.17 | 0.85
xylitol2 | 2.78 | 3.04 | 9.77 | 17.4 | 21.4
xylitol3 | 3.62 | 2.82 | 11.9 | 21.6 | 21.7
xylitol4 | 3.36 | 3.91 | 10.2 | 19.3 | 21.5
glucose2 | 26.7 | 0 | 0 | 0 | 0
glucose3 | 24.4 | 0 | 0 | 0 | 0
Repeated batch culture using immobilized C. magnolliae
 | Xylitol conc. | Xylitol yield | Xylitol productivity | Ethanol productivity
1 | 16.8 g/L | 68 % | 0.25 g/L/h | -
2 | 21.4 g/L | 67 % | 0.26 g/L/h | 4.49 g/L/h
3 | 21.7 g/L | 71 % | 0.26 g/L/h | 3.36 g/L/h
4 | 21.5 g/L | 68 % | 0.26 g/L/h | 5.38 g/L/h
YA167
Immobilized yeast
Cultivation
Settlement
Withdrawal of culture broth
Addition of medium
Repeat batch culture with immobilized bacteria
Conclusions
・Co-cultivation of C. magnoliae and S. cerevisiae was successfully performed
using an air-lift bioreactor.
・4 cycle of repeated culture was demonstrated.
・Further research is required to improve xylitol productivity.